## Slide 1: Protocol Independent Forwarding (PIF) project
ONF SDN Evolution workday session / September, 2016

## Slide 2: PIF Open Source SDN software project … and also ONF Specifications Area group
Intermediate representation
P4
PX
PIFL
Focus areas of PIF project:
Intermediate Representation elements
Use cases
Runtime APIs
Feeds into ONF “SDN Evolution” specification activity

## Slide 3: BIR (pronounced “beer”): the “B” IR
Intended to capture the different threads of IR-related discussions
Intended to be at the “right” level for this domain-specific IR
Intended to be more language/target neutral than the AIR strawman
Candidate as programmable datapath model for evolved SDN
Open source software simulator based on Meta-IR infrastructure

## Slide 4: Main influences
BIR
PIF group discussions
P4, RMT, AIR
school
POF
school
NetASM, Banzai
school
PX
school
rather than
Design

## Slide 5: The BIR packet processing model
Top-level static packet data flow graph (linear pipeline at first)
  User-defined metadata collection(s) associated with each packet in transit
Each node is a “packet processor”
  Either a “control flow”: programmed processor
  Or an “other processor”: supplied processor
Could be described as “µVNF chaining”
A control flow involves traversing “basic blocks” to completion
A basic block:
  Has optional defined local contexts of: header type, table
  Is passed a packet and an offset into that packet
  Carries out an unconditional sequence of header/metadata updates and/or calls on library methods
  Calculates next offset and next basic block at end

## Slide 6: Control Flow motivation
Recognizes that packet processing is driven by two dynamic factors:
  Packet data (data plane input)
  Table data (control plane input)
Therefore, context for a basic block:
  Particular header in packet: can be read or written
  Particular table:
    Lookup takes a struct containing expressions for values
    Result is a struct containing values: some can be decoded as actions
Metadata collections can be associated with each packet
  Can represent fine- and coarse-grain parsing and match-action pipelines

## Slide 7: Example: Three-stage processor pipeline
Control Flow
Start Control State
Compute Packet_offset
Select Basic_block
Basic Block
Instruction 1
Instruction 2
. . .
Instruction N
Next Control State
Compute Packet_offset
Select Basic_block
Header format
Other Processor
Control Flow
Terminate
Terminate
BB
BB
BB
BB
BB
Start Control State
BB
BB
BB
BB
BB

## Slide 8: BIR open source software
GitHub:
  OpenNetworkingFoundation/PIF-Open-Intermediate-Representation
Refactoring of original PIF AIR-IRI software framework
  Meta-IR for defining experimental IRs
  BIR model defined using Meta-IR
  Switches defined as BIR instances
YAML used to represent BIR model, and BIR-defined switches
Some to-do items …

## Slide 9: BIR technical report
Currently version 1.1 – updated version 1.2 imminent
  In the OSSDN PIF GitHub repository
  Also in the ONF ARO repository
Open for wider (extra-PIF) review
Appendix summarizes some issues under discussion
Step towards a ONF “Open IR” specification

## Slide 10: Runtime API setting
Intermediate representation
P4
PX
PIFL
HLL’s API
IR’s API
Target’s API
Adapter
Adapter
Generates
Generates

## Slide 11: Summary of PIF work areas
Experimentation with IR features and capabilities:
  to lead to a final IR proposal
Investigating diverse use cases for the IR:
  to ensure apt coverage
Runtime API for the IR:
  to feed into next-generation OpenFlow

## Slide 12: How to join in the PIF project
PIF Open Source SDN project at:
  https://groups.opensourcesdn.org/wg/PIF/dashboard
  Contains calendar, mail archive, documents, etc.
PIF GitHub:
  https://github.com/OpenNetworkingFoundation/PIF-Open-Intermediate-Representation
Join the weekly call:
Tuesdays 11am -12 noon Pacific
See calendar entry for full information
Join the mailing list (pif@community.opensourcesdn.org)